Project file format
Offset	Size	Description	Responsibility
0	4	Project file version	ExecFileManager
4	1	Executable file format	ExecFileManager

5	4	Executable file size	TExecutableFile
9	4 + P	Executable file full path	TExecutableFile
		Regions	TRegions
P+13	4	Number of Sections	TExecutableFile
P+17	S	Sections

T+S+17	H	Important executable file header information	TExecutableFile descendants

Sections array item
Offset	Size	Description	Responsibility
0	1	Section type	TExecutableFile
1	4 + N	Section name	TSection
N+5	4	Section index in TExecutableFile.Sections	TSection
N+9	S	A Section	TSection descendants

Code Section
Offset	Size	Description	Responsibility
	4	Section index among code section
	4	Bit32
	4	Section's file offset
	4	Section's file size
	4	Memory offset
	4	Memory size
	4	Code size
	1	Has Entry point
	4	Entry point address

	4	InstructionLineCount
	4	DataLineCount
	4	ReferenceLineCount
	4	BlankLineCount
		// Statistics
	4	LastItem code index
	1	IsDisassembled
	4	Disassembled count
	4	InstructionsCount

	CodeSize	Code array
	CodeSize	DisassemblerMap

Import section
Offset	Size	Description	Responsibility
0	4	TotalFunctionCount
4	4	ModulCount
		Moduls
0	4 + N	Modul name
N+4	4	Functions' count
		Functions of module
	SizeOf - 8	Function
0	4+N	Function name
N+4	4	Occurence count
		Occurence
0	4	Occurence address

Export section
Offset	Size	Description	Responsibility
0	4	Function count
		Functions
	SizeOf - 4	Function
	4+N	Function name